## Slide 1: Energy Transfer in Kitchen Appliances
An overview
Dr Simon Batchelor
May 2023

## Slide 2: Introduction
In the Water Boiling Test WBT (and in many other assessments of thermal efficiencies), the protocol prescribes 3 test phases –
  i) raising a specified amount of water or food to a given temperature from a cold start,
  ii) raising a specified amount of water or food from a hot start, and
  iii) simmering said water for a given time (generally 45 minutes, but in some protocols 30mins). ‘Simmering’ while generally applied to a stew or water-based food, can be interpreted as ‘holding the water or food at a prescribed temperature’.
Cooking is more complex than boiling water, and so some devices such as air fryers, ovens, grills cannot be tested by the conventional WBT.
However, in the following we have taken our cue from the WBT and considered the 2 key phases to energy efficiency in cooking:
Heating of the pot of food
  Slides 3 to 6 consider how a device raises the temperature of the food
Losses during cooking of the food
  Slides 8 onwards consider how the food is maintained at temperature

## Slide 3: Phase 1 – Heating of the pot

## Slide 4: Resistive heating element (hotplate)
Heat generated in plate by passing current through a resistive element.
Relies on contact to transfer heat by conduction (and a little radiant)
Can be AC or DC, depends on current and voltage and resistance.
Easy to make and easy to adapt – operation is on and off controlled by thermostat.
Can use any material for the pot
Heat transfer to pot dependent on fit of pot to top of heating element.
If pot has dents, some bits don’t touch
If pot significantly smaller then loss at edges
Resistive heating element
Cooking pot
Badly made heating elements lose heat downwards as the base is open.
Image credit - freepik
If pot significantly smaller than heating element then there are losses at the edges

## Slide 5: Infra-red heating element.
Infrared heating element
Cooking pot
Heat generated in plate by passing current through a resistive element such that heat transfer is through infrared.
Relies on radiant transfer of heat
Can be AC or DC, depends on current and voltage and resistance.
Easy to make and easy to adapt – operation is on and off controlled by thermostat.
Can use any material for the pot
Heat transfer to pot possible even with an air gap.
Less concern about pot dents, heat transfer across small air gaps
If pot significantly smaller than heating element then there are losses at the edges
Most constructed with reflective base, so few losses downward.
Image credit - freepik

## Slide 6: Induction heating of a pot
Induction coil
Cooking pot
Heat generated in the pot by fluctuating magnetic field
Low frequency AC is converted to DC and back to high frequency AC. DC input is also possible.
Operation relies on the electronics.
Pot has to be iron based.
Heat generated in the pot, energy transfer very slightly sensitive to distance to pot.
If pot has dents, induction sensitive to distance to metal of pot.
If pot significantly smaller then NO loss at edges
NO heat loss downwards
Image credit - freepik

## Slide 7: Most electric pressure cookers use resistive heating elements because heat transfer assured by design:-
Reistive heating element
Cooking pot
Has a bespoke pot, that is correct size for heating element and…
Heat generated in plate by passing current through a resistive element.
Can be AC or DC, depends on current and voltage and resistance.
Easy to make and easy to adapt - operation is on and off controlled by thermostat.
Pot base slightly concave as required for pressure cookers ISO, and therefore heating element slightly convex to fit pot – contact between the two is excellent. (Also heating element slightly smaller than pot, so no side leakage)
Pot has no dents
Pot is fit to heating element diameter (often fractionally bigger)
Heating element is enclosed so downward losses minimal.
Image credit ajay_suresh

## Slide 8: Phase 2 – losses during cooking
Transferring heat into the pot is only half the issue when it comes to considering energy efficiency.
As said slide 2, WBT iii) considers energy required to hold the water at just below 100 degrees for a given time (i.e. ‘simmering’).
If you simmer a food (like beans in water) for 30 minutes or more, then the losses from your cooking device mount up.
Energy efficient devices for long cooking (e.g. over 20 mins) include insulation to mitigate those losses.
Cooking variously includes frying, baking and simmering (among other processes), and some task specific appliances cannot ‘simmer’. We have interpreted the simmering phase as ‘holding the food at a specified temperature for a given period of time’.

## Slide 9: Losses during cooking – no insulation True for either induction, resistive hotplates, infra-red
Lid is important.
Radiant heat emitted from pot sides (can be about 400W)
  So once at temperature (100deg) 30 min simmer is 0.2kWh
While simmering, the resistive heating element or infrared or induction tries to compensate for losses, judging when to come on by a thermostat.
Control becomes important
  If thermostat is analogue, based on a dial, then off and on could boil the water rapidly, and losses greater due to evaporation. Control is down to preferences and skill of the cook - they decide where to put the dial
  If thermostat is more precise (generally but not exclusively digital), then simmering can be held at a precise temperature just below boiling point – evaporation losses minimal.
Cooking pot
Cooking pot
For short stir fry or quick cooking in a frying pan, then losses during the cooking phase are minimal – heat in the pot doesn’t have the time to go out from the pot, and the surface area of the sides is small.

## Slide 10: Electric pressure cookers minimize losses by
Temperature control is based on a switch triggered by the pressure – so very precise temperature control.
Once at pressure, heating element barely comes on, losses are minimal so cooking continues with minimal new heating energy coming into the system.
Cooking pot
Air gap between pot and outside world. Air is low conduction, and inside of outer wrap reflects back the radiant heat.
Lid is tight to form the pressure seal. But even without pressure, the lid is a good fit minimizing losses.
Without pressure and at simmering temperature (100deg) 30 min simmer is about 0.02kWh (which was 0.2kWh uninsulated).
With pressure the food is at between 108 and 116 deg, and therefore cooks faster.
Utilises good stage 1 heat transfer to pot as pot sized to fit resistive heater.
Image credit ajay_suresh
Also faster cooking due to pressure so 2 hour simmer of beans would only need less than 30 mins because of the pressure effects.
Needs less energy to cook than uninsulated devices.

## Slide 11: Slow cookers minimizes losses by
Temperature control is based on a thermostat.
Depending on quality, there is insulation or an air gap between pot and outside world.
Lid is tight but not sealed. But even without pressure, the lid is a good fit minimizing losses.
Not always the most energy efficient as insulation not always the best – so slow that losses for a cooked meal are almost as much as without insulation.
Resistive heating element
Cooking pot
Utilises good stage 1 heat transfer to pot as pot sized to fit resistive heater.
Image credit - Bunches and Bits {Karina}

## Slide 12: Rice cookers minimize losses by
Temperature control is based on a thermostat. Keeps it at or just below boiling. If the base gets dry then it switches off (rice must be done)
Depending on quality, there is insulation or an air gap between pot and outside world.
Lid is tight, almost sealed. Without pressure but the lid is a good fit minimizing losses.
Short duration of rice making makes this a very energy efficient but task specific product.
Resistive heating element
Cooking pot
Can be used for other cooking, but the thermostat prevents frying.
Utilises good stage 1 heat transfer to pot as pot sized to fit resistive heater.
Image credit: The Marmot

## Slide 13: Multi cookers minimize losses by
Temperature control is based on a thermostat.
However, in contrast to a rice cooker, the thermostat will allow 140 degree frying.
Depending on quality, there is insulation or an air gap between pot and outside world.
Lid is tight, almost sealed. Without pressure but the lid is a good fit minimizing losses.
Resistive heating element
Cooking pot
Very variable overall efficiency – dependent on thermostat control and whether it has some insulation
Utilises good stage 1 heat transfer to pot as pot sized to fit resistive heater.
Image credit :wilko.com

## Slide 14: ISEC (insulated Solar Electric Cookers (origin California, now in 8 countries) minimize losses by
No temperature control on most – relies on being low power to not overheat (between 100 and 400W).
Thick quality insulation between pot and outside world is a key point of the device. When using thermal storage the heater heats the mass or phase change material, and then the heating of the pot is ‘boosted’ by the thermal store.
Lid can be tight, almost sealed. Without pressure but the lid is a good fit minimizing losses.
Resistive heating element
Cooking pot
Very variable overall efficiency dependent on quality of the insulation and its construct.
Utilises good stage 1 heat transfer to pot as pot sized to fit resistive heater.
Sometimes with Thermal storage
Image credit – P Schwartz

## Slide 15: Fan assisted ovens minimize losses by
Temperature control is based on a thermostat.
Can get to 200 degrees+.
The fan ensures even distribution of heat, while the pot (or baking tray) sits on a shelf – not touching the resistive heaters. (Can also be infra-red heaters)
Door opens sideways. Most ovens are well sealed, but seals weaken over time. Most don’t have active insulation but rely on an air gap in the glass door, and the mass of the oven.
Resistive heating element
Cooking pot
Very variable overall efficiency – fan ovens are twice as efficient as same configuration of oven without a fan.
Flexible pot and pan sizing, baking tray etc, as the environment around it is heated.
Heating elements may be in base, sides or ceiling
Photo credit – Trusted reviews.

## Slide 16: Air fryers minimize losses by
Temperature control is based on a thermostat.
Can get to 200 degrees+.
The fan ensures even distribution of heat, while the pot allows for air flow – not touching the resistive heaters. (Can also be infra-red heaters)
Accessed via a tray that pulls out sideways. Most air fryers relatively well sealed, but the inner pot itself has no ‘lid’ to keep air flow max. ‘Chips and Sausages’ added directly to air-fryer inner pot which has holes in base, dripping juices onto inner base.
Cooking pot
Very efficient because basically a small fan oven without large thermal mass in the walls.
Pot comes with device, and environment around it is heated. Generally access is a tray that pulls the pot out.
Heating elements generally at the top (ceiling). Can sometimes give a ‘grill’ effect depending on type.
Photo credit: Marco Verch

## Slide 17: Final comment
There are other devices not covered in this slide deck, eg Kettles, toasters, grills, among others.
New configurations of multi cookers are appearing – e.g. Hotpot grills which combine hotplates and tight control of temperature during simmering (but don’t have insulation)
Induction is seen as the best for Phase 1 heat transfer, but this is only the case when compared to resistive heating and infra-red with a poorly matched pot.
The MECS programme has an ever growing body of test data on these devices both in lab settings and in real world use. For more information please consult our website www.mecs.org.uk (particularly the ecookbooks)
Please note this slide deck is based on the WBT, but MECS as a research programme believes every appliance should be tested with other protocols. At a minimum - Controlled Cooking Tests (CCT) (cooking a pre-determined local meal) to ensure a cultural fit to food, and piloted use in Kitchen performance test preferably over time (what we call cooking diaries).
Photo Credit Amazon